## Slide 1: ELECTRICAL AND ELECTRONICS ENGINEERING & USER INTERFACE
Short term load forecasting using ANN
Team Members
Group - 13
Adhwaidh K - CB.SC.U4AIE24003
Adith S - CB.SC.U4AIE24004
Chaitanya Varma - CB.SC.U4AIE24017

## Slide 2: Introduction
Electricity demand forecasting is vital for efficient energy production and distribution.
Short-term load forecasting (STLF) helps utility companies plan power generation and reduce operational costs.
This project uses historical weather and load data to predict future energy demand.

## Slide 3: Literature Review
S. No. | Title | Year | Methodologies | Key Contributions
1. | The Short-Term Load Forecasting Using an Artificial Neural Network | 2021 | ANN | Analyzed daily and weekly variations in historical loads to enhance forecasting accuracy.
2 | Short Term Load Forecasting Using Artificial Neural Network | 2017 | ANN | Addressed load forecasting by considering different load profiles for weekdays and weekends.
3 | Short-Term Aggregated Residential Load Forecasting using BiLSTM and CNN-BiLSTM | 2023 | BiLSTM, CNN-BiLSTM | Investigated the capabilities of BiLSTM and CNN-BiLSTM models for day-ahead forecasting at an hourly resolution.

## Slide 4
S. No. | Title | Year | Methodologies | Key Contributions
4. | Short Term Load Forecasting by Artificial Neural Network | 2017 | ANN | Established a short-term load forecasting model emphasizing its transparent structure and ease of implementation.
5. | Short-Term Load Forecasting Using an LSTM Neural Network for a Colombian Grid Operator | 2023 | LSTM Neural Network | Proposed a neural network-based model to forecast short-term load for a Colombian grid operator, considering a seven-day time horizon.
6, | Electric Load Forecasting Using an Artificial Neural Network | 1991 | Backpropagatio n Algorithm | Proposed a nonlinear load model using backpropagation for electric load forecasting.

## Slide 5
S. No. | Title | Year | Methodologies | Key Contributions
7. | Short-Term Load Forecasting Using Artificial Neural Networks | 2019 | Multistage ANN | Discussed the systematic design of a multistage ANN-based short-term load forecaster.
8. | Short-Term Load Forecasting using a Cluster of Neural Networks for Residential Load | 2016 | Cluster of Neural Networks | Proposed a model for next-day load forecasting in hourly steps using a cluster of neural networks.
9. | A Comparative Assessment of Deep Learning Models for Day-Ahead Load Forecasting: Investigating Key Accuracy Drivers | 2023 | Deep Learning Models | Conducted a comparative study of deep autoregressive models for day-ahead load forecasting.
10. | Appliance Level Short-term Load Forecasting via Recurrent Neural Network | 2021 | RNN | Presented an STLF algorithm for predicting power consumption of individual electrical appliances.

## Slide 6: Research Gaps
Lack of Nonlinearity Handling: Traditional models fail to capture complex patterns.
Limited Weather Impact Consideration: Many studies do not include temperature, etc.
Lack of Real-Time Forecasting: Some models require high computation time.
Limited Deployment: Few models integrate a user-friendly web interface.

## Slide 7: Problem Statement
Inaccurate forecasting leads to wastage of resources or failure in meeting demand.
Need for an intelligent system to predict load with high accuracy using weather conditions, time-based features, and historical data.

## Slide 8: Objectives
Develop a data-driven model for short-term electrical load forecasting.
Integrate various features like weather data, time, and historical load values.
Use regression and neural networks for improved forecasting accuracy.
Display forecast results in a user-friendly GUI interface.

## Slide 9: Dataset
Time-Based Data:
The dataset contains hourly records (datetime) spanning multiple weeks.
hourOfDay column indicates the hour of the day (0-23).
Historical Load Data:
week_X-2, week_X-3, week_X-4: Electricity demand from past weeks, useful for forecasting.
MA_X-4: Moving average of demand, helping smooth fluctuations.

## Slide 10
Target Variable:
DEMAND: Represents actual electricity demand, crucial for training ANN models.
Day and Special Events:
dayOfWeek: Represents the day (e.g., 1 = Monday).
weekend: Indicates if the day is a weekend (1 for weekend, 0 for weekday).
holiday & Holiday_ID: Identifies public holidays, affecting demand.
Weather Impact:
T2M_toc: Temperature variable, which influences power consumption trends.

## Slide 11: Flow Chart
Figure 1.1
13

## Slide 12: Methodology
Data Collection & Preprocessing:
Load data from an Excel file.
Handle missing values and remove constant features.
Deal with multicollinearity using correlation analysis.
Feature Engineering:
Incorporate historical loads (previous day/week same hour).
Use time-related and weather features like temperature, hour, weekend, holidays.

## Slide 13
Modeling Techniques:
Train a feedforward neural network with 30 neurons in the hidden layer.
Performance Metrics:
Calculate MAE (Mean Absolute Error) and MAPE (Mean Absolute Percentage Error).
Assess forecast accuracy and visualize results.
GUI Integration:
Forecast results saved as a .json file.
GUI displays load predictions, errors, plots, and interactive feedback sections.

## Slide 14: Results

## Slide 26: Conclusion
The neural network-based approach provided high forecasting accuracy.
GUI implementation makes the system user-friendly for non-technical users.
The methodology handles noisy, missing, and redundant data efficiently.

## Slide 27: Future Scope
Include real-time data streaming from smart meters or IoT sensors.
Add deep learning models like LSTM for improved time-series predictions.
Expand to mid/long-term load forecasting.
Introduce grid optimization and price prediction modules.

## Slide 28: References
[1] J. Doe, "Electric Load Forecasting Using ARIMA," IEEE Transactions on Power Systems, vol. 35, no. 4, pp. 1234-1245, 2017.
A. Smith, "Deep Learning for Power Demand Prediction," Energy Informatics Journal, vol. 28, no. 2, pp. 78-90, 2019.
[2] D. C. Park, M. A. El-Sharkawi, R. J. Marks II, L. E. Atlas, and M. J. Damborg, "Electric Load Forecasting Using an Artificial Neural Network," IEEE Transactions on Power Systems, vol. 6, no. 2, pp. 442-449, 1991.
[3] S. Kumar and S. Jain, "Short Term Load Forecasting Using Artificial Neural Network," 2017 International Conference on Computing, Communication and Automation (ICCCA), Greater Noida, India, 2017, pp. 633-637.
[4] Y. Zhang, J. Wang, and X. Wang, "The Short-Term Load Forecasting Using an Artificial Neural Network," Complexity, vol. 2021, Article ID 1502932, 2021.

## Slide 29: Thank You!